## Slide 1: Roadside Vegetation Barrier Designs to Mitigate Near-Road Air Pollution Impacts
K. Max Zhang
Sibley School of Mechanical and Aerospace Engineering
Cornell University

## Slide 2: Acknowledgments
Current and former PhD students working on this subject: Zheming Tong, Jon Steffens, and Bo Yang
Valuable discussions with Drs. Rich Baldauf, Vlad Isakov and Parik Deshmukh at USEPA
Experimental data from USEPA

## Slide 3: Relevant Properties and Processes
Dispersion
Deposition
Aerosol dynamics and gas chemistry
Leaf area density/porosity
Drag coefficient
Width, height
Barrier layout
VOC emissions
Wind speed, direction
Atmospheric stability
Highway geometry
Road properties
Traffic conditions (volume, mix, etc.)
Surrounding structures
Particle size distribution
Concentrations of air toxics
Human exposure
Design parameters

## Slide 4: More on the Atmospheric Processes
Dispersion
  Solid barrier effect: creating upward momentum and enhancing plume dispersion -> lower ground level conc. behind the barrier
  Windbreak effect: plume going through the canopy at slower speed -> higher ground level conc.
  On-road accumulation: higher on-road conc., but lower ground level conc. behind the barrier
Deposition
  Size dependent
  Time dependent
  Re-suspension?
Aerosol dynamics and gas chemistry

## Slide 5: Comprehensive Turbulent Aerosol and Gas Chemistry (CTAG)

## Slide 6: Past work on Transportation and Air Quality

## Slide 7: Revisiting Chapel Hill Experimental Dataset with Large Eddy Simulation (LES)
The Chapel Hill (NC) dataset was collected by USEPA and Duke researchers (Hagler et al., 2011).
Steffens et al. (2012) employed RANS turbulence model and two different particle deposition models to simulate the dataset.
We recently applied the Large Eddy Simulation (LES) model to re-simulate the dataset.
LES model shows generally good agreement.
Tong et al., manuscript in preparation

## Slide 8: Design Configurations
Tong et al., manuscript in preparation

## Slide 9: Main Assumptions
Highway conditions are taken as the same as those in the Chapel Hill experiment
Infinite long barrier
Baseline case:
  Leaf area density and drag coefficient taken from the Chapel Hill experiment (conifer)
  Perpendicular wind direction

## Slide 10: Case 1: Horizontal Gradient
15m
Baseline Top View
Tong et al., manuscript in preparation

## Slide 11: Case 1: Particle Size Distribution
Tong et al., manuscript in preparation

## Slide 12
Solid barrier: significant reduction in conc. behind the barrier with on-road accumulation
Green Wall: Slight more reduction compared to the solid barrier case
Vegetation-solid barrier combination: greatest reduction in conc. behind the barrier with on-road accumulation
Cases 2, 3, 4: Solid, Green Wall and Combination
Tong et al., manuscript in preparation

## Slide 13: Sensitivity: Leaf Area Density (LAD)
Increasing LAD
Increasing LAD leads to more deposition and upward momentum
  For smaller particles, greater reduction behind the barrier
  For larger particles with relatively small deposition velocity, approaching the behaviors of a solid barrier
Tong et al., manuscript in preparation

## Slide 14: Sensitivity: Barrier Width
Increasing width
Increasing width leads to more deposition
  For smaller particles, greater reduction behind the barrier
  For larger particles with relatively small deposition velocity, earlier transition to lower conc. compared to the no-barrier case
On-road accumulation is modest compared to solid barrier
Tong et al., manuscript in preparation

## Slide 15: Sensitivity: Wind Direction
The degree of on-road increase is contingent on oncoming wind direction.
The on-road concentration decreases with more parallel wind to the road
Tong et al., manuscript in preparation

## Slide 16: Edge Effects
Steffens et al. (2013)
Steffens et al. (2014)

## Slide 17: Report Card for Model Capability
Modeling results capture the general phenomena very well
  Vegetation-solid barriers show greatest reduction
  Wider and denser trees lead to more reduction
  Edge effects can be captured
  …
Research needs
  More testing against different vegetation barrier configurations, meteorological and traffic conditions
  Turbulence modeling: drag vs. wind speed
  Deposition modeling
  Effects of vegetation barriers on near-source chemistry and regional ozone chemistry
  Parameterization
  …

## Slide 18
Baldauf et al., manuscript under review
The effect of wind direction on on-road concentrations
White: On-road; Shaded: Barrier